## Slide 1: ITD + ASA 5585-X Configuration Guide
Don Garnett
Mouli Vytla
Revision 1.4

## Slide 2
Document revision updates
19-August 2015 (version 1.4) – Don Garnett
Changes:
Updated topology diagrams with 2015 PPT icons
Added logical views
Added ASA Clustering section
Added information regarding L3 over VPC, peer VDC, other optional parameters
Added optional ITD parameters
Information regarding Device Group options such as HA config options will be added soon.
21-November-2014 (version 1.3) – Mouli Vytla
Changes:
Added dual-VDC (non-VPC) Sandwich mode configuration for ASA + ITD
23-June-2014 (version 1.2) – Don Garnett
Changes:
Removed Static Routes configuration from N7K –not needed
Removed VIPs from ITD Processes –not needed
Revised Auto-Configuration and Verification Sections to reflect configuration output without VIPs in place

## Slide 3: N7K ITD and ASA Deployment Methods
ITD with Firewall on a Stick (One Arm) This design uses a single VDC with a single 802.1q interface (or .1q port-channel) connecting to the ASAs. The ASAs do traffic filtering and Inter-Vlan routing by means of splitting the single interface into sub-interfaces.
ITD with Single VDC (Two Arm) This design uses a single VDC with 2 separate (access or trunk) interfaces connecting to the ASAs. The ASAs filter traffic traversing the 2 interfaces. Traffic is segregated on the switch by VRFs to ensure traffic is inspected by the firewalls.
ITD with Dual VDC Sandwich This design leverages 2 VDCs, each with an interface connecting to the ASAs. The ASAs filter traffic traversing the 2 VDCs. This design could also be used with separate N7K switches instead of VDCs if desired.
ITD with Dual VDC (vPC) Sandwich This design leverages 2 VDCs, each with an interface connecting to the ASAs. The ASAs filter traffic traversing the 2 VDCs. This design could also be used with separate N7K switches instead of VDCs if desired. Two N7k switches are deployed in vPC mode
Cluster Deployments Cluster deployments can encompass any of the above methods. VPC Peers with Dual VDC Sandwich is demonstrated in this document.

## Slide 4
Single VDC
Firewall on a Stick Topology
Logical separation of traffic across ASA interfaces using 802.1q tagging

## Slide 5
ASA1
ASA2
ASA3
ASA4
.111
Single VDC ‘Firewall on a Stick’ Topology
NXOS GBR 7.2 L3 Over VPC
Sw1
DC1-N7K-7
Sw2
DC1-N7K-8
VPC trunks
connect to each firewall
.112
.113
.114
Outside
Port-Channel 21.100
VLAN 100
VRF Outside
10.0.0.111 – 114/24
Inside
Port-Channel 11.101
VLAN 101
10.1.0.111 – 114/24
Firewall Sub-Interfaces
SVI VLAN 100 – 10.0.0.18
VRF FW_OUTSIDE
Vl101 – 10.1.0.18
NX Transit Interfaces
SVI VLAN 1100 – 10.100.0.1 (HSRP) VRF FW_OUTSIDE
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interfaces
10.0.0.114 Outside
10.1.0.114 Inside
VPC Peer Link
ITD
ITD
SVI VLAN 100 – 10.0.0.17 VRF FW_OUTSIDE
SVI VLAN 101 – 10.1.0.17
SVI VLAN 1100 – 10.100.0.1 (HSRP) VRF FW_OUTSIDE
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interfaces
NX Transit Interfaces
Logical View

## Slide 6
ASA1
ASA2
ASA3
ASA4
.111
Single VDC ‘Firewall on a Stick’ Topology
NXOS 6.2.10 – 7.1
Sw1
DC1-N7K-7
Sw2
DC1-N7K-8
Single trunk interface
connects to each firewall
.112
.113
.114
SVI VLAN 100 – 10.0.0.17 VRF FW_OUTSIDE
SVI VLAN 101 – 10.1.0.17
SVI VLAN 1100 – 10.100.0.1 (HSRP) VRF FW_OUTSIDE
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interfaces
Outside
TenGigabitEthernet0/6.100
VLAN 100
VRF Outside
10.0.0.111 – 114/24
Inside
TenGigabitEthernet0/6.101
VLAN 101
10.1.0.111 – 114/24
Non-VPC port-channels can also be used
Firewall Sub-Interfaces
NX Transit Interfaces
SVI VLAN 100 – 10.0.0.18
VRF FW_OUTSIDE
Vl101 – 10.1.0.18
NX Transit Interfaces
SVI VLAN 1100 – 10.100.0.1 (HSRP) VRF FW_OUTSIDE
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interfaces
10.0.0.114 Outside
10.1.0.114 Inside
VPC Peer Link
ITD
ITD
Logical View

## Slide 7
Single VDC ‘Firewall on a Stick’ Topology
Logical View
VLAN 1100
VLAN 100
VLAN 101
VLAN 1101
ITD
ITD
Single VDC
VLAN + VRF Separation
VRF Red – Outside
VRF Blue - Inside

## Slide 8
Nexus 7000
Enable Features
Enable L2 Vlans to be used in the topology
Configure VPC between local and peer switch –Optional
  - Enable L3 Over VPC feature (NXOS 7.2+ only)
Create VRF(s) needed for ITD process
Configure (physical/logical) transit switch interfaces connecting to firewalls Inside and Outside interfaces
Configure ITD Ingress interfaces that connect to downstream network infrastructure
Define ITD Device Groups and Health Probe parameters
Configure ITD service and mandatory parameters
Enabled optional ITD features
Configuration Steps – Nexus 7000
Configuration steps are shown using NXOS 7.2+ topology

## Slide 9
1. Enable Features
feature pbr
feature interface-vlan
feature hsrp #optional
feature lacp #optional
feature vpc #optional
feature sla sender
feature sla responder
feature itd
2. Enable L2 Vlans used in topology
vlan 1,100-101,1100-1101
Configuration Steps – Nexus 7000

## Slide 10
3. Configure VPC between local and peer switch. Enable L3 Over VPC (NXOS 7.2+ only) –Optional
vrf context vpc-keepalive
vpc domain 1
peer-keepalive destination 1.1.1.7 source 1.1.1.8 vrf vpc-keepalive
peer-gateway
layer3 peer-router
ipv6 nd synchronize
ip arp synchronize
interface port-channel1
description - VPC PEER LINK
switchport
switchport mode trunk
spanning-tree port type network
vpc peer-link
interface Ethernet1/1
description - VPC KEEP-ALIVE LINK
vrf member vpc-keepalive
ip address 1.1.1.8/24
no shutdown
interface Ethernet1/2-3
description - VPC PEER LINK
switchport
switchport mode trunk
channel-group 1 mode active
no shutdown
Configuration Steps – Nexus 7000

## Slide 11
4. Create VRF(s) needed for ITD process –Optional
vrf context FW_OUTSIDE
#In this configuration, Outside traffic heading to the firewall will use the FW_OUTSIDE VRF. After entering and exiting the firewall the traffic will use the default VRF. Traffic is directed to individual firewalls via PBR, thus routes are not needed.
Configuration Steps – Nexus 7000

## Slide 12
5. Configure (physical/logical) switch transit interfaces that connect to firewall Inside and Outside interfaces
interface Vlan100
description OUTSIDE_FW_VLAN
vrf member FW_OUTSIDE
no ip redirects
ip address 10.0.0.138/24
hsrp 3
ip 10.0.0.100
interface Vlan101
description INSIDE_FW_VLAN
no ip redirects
ip address 10.1.0.18/24
hsrp 1
ip 10.1.0.10
interface Ethernet4/25
description To_ITD-ASA-1_PortChannel
switchport mode trunk
switchport trunk allowed vlan 100-101
channel-group 11 mode active
interface Ethernet4/26
description To_ITD-ASA-2_PortChannel
switchport mode trunk
switchport trunk allowed vlan 100-101
channel-group 12 mode active
Replicate for every connecting ASA
Configuration Steps – Nexus 7000
interface Port-Channel11
description VPC_TO_ASA1
switchport mode trunk
switchport trunk allowed vlan 100-101
vpc 11
interface Port-Channel12
description VPC_TO_ASA1
switchport mode trunk
switchport trunk allowed vlan 100-101
vpc 12
interface Port-Channel13
description VPC_TO_ASA3
switchport mode trunk
switchport trunk allowed vlan 100-101
vpc 13
interface Port-Channel14
description VPC_TO_ASA4
switchport mode trunk
switchport trunk allowed vlan 100-101
vpc 14
Replicate for every connecting ASA

## Slide 13
6. Configure ITD Ingress interfaces which connect to downstream network infrastructure.
interface Vlan1100
description EXTERNAL_to_FW-OUTSIDE
no shutdown
vrf member FW_OUTSIDE
no ip redirects
ip address 100.100.0.18/24
hsrp 100
ip 100.100.0.1
interface Vlan1101
description INTERNAL_to_FW-INSIDE
no shutdown
no ip redirects
ip address 10.101.0.18/24
hsrp 1
ip 10.101.0.1
interface port-channel41
description BUNDLE_FOR_AGGREGATE_TRAFFIC
switchport
switchport mode trunk
switchport trunk allowed vlan 1100-1101
vpc 41
interface Ethernet10/1-8
switchport
switchport mode trunk
switchport trunk allowed vlan 1100-1101
channel-group 41
no shutdown
Configuration Steps – Nexus 7000

## Slide 14
7. Define ITD Device Groups and Health Probe parameters
itd device-group FW_INSIDE
#Config Firewall Inside interfaces as nodes
node ip 10.1.0.111
node ip 10.1.0.112
node ip 10.1.0.113
node ip 10.1.0.114
probe icmp frequency 5 timeout 5 retry-count 1
itd device-group FW_OUTSIDE
#Config Firewall Outside interfaces as nodes
node ip 10.0.0.111
node ip 10.0.0.112
node ip 10.0.0.113
node ip 10.0.0.114
probe icmp frequency 5 timeout 5 retry-count 1
Probe Default Values switch(config-device-group)# probe icmp frequency 10 retry-down-count 1 retry-up-count 1 timeout 5
Configuration Steps – Nexus 7000

## Slide 15
8. Configure ITD service and mandatory parameters
itd INSIDE
device-group FW_INSIDE
#binds inside firewall interfaces to process
ingress interface Vlan1101
#applies ITD route-map to Vlan1101 interface
failaction node reassign
#dictates to use the next available Active FW if a FW goes offline
load-balance method src ip
#load balances traffic applicable in buckets to firewalls based on source-IP address (default).
no shut
itd OUTSIDE
vrf FW_OUTSIDE
#applies this ITD process to the defined vrf named ‘FW_OUTSIDE’
device-group FW_OUTSIDE
ingress interface Vlan1100
failaction node reassign
load-balance method dst ip buckets 16
#load balances traffic applicable in buckets to firewalls based on destination. Default is src-ip (itd INSIDE)
no shut
Configuration Steps – Nexus 7000

## Slide 16
9. Configure optional ITD features
N7K-1(config)# itd INSIDE
N7K-1(config-itd)# ?
access-list ITD access-list name ##Traffic to include in LB Profile
device-group ITD device group
exclude ACL to exclude from redirection ##Traffic to exclude from LB Profile
failaction ITD failaction
ingress ITD ingress interface
load-balance ITD Loadbalance ##Configures bucket allocation, mask position, or Src/Dst LB Method
nat Network Address Translation ##Enables NAT Based ITD instead of PBR based (default)
no Negate a command or set its defaults
peer Peer cli for sandwich mode failure notification ##Enables awareness of ITD process state in another VDC (used for 2-Arm/Sandwich ITD configurations)
shutdown
virtual ITD virtual ip configuration ##Global and Device-group specific VIP configuration
vrf ITD service vrf
Configuration Steps – Nexus 7000

## Slide 17
Configuration Steps – ASA Firewall
ASA Basic Configuration: There is nothing ITD specific about configuring the ASA for ITD. The following interface configuration is used with this topology.
interface Port-channel11
nameif aggregate
security-level 100
no ip address
!
interface Port-channel11.100
description OUTSIDE
vlan 100
nameif outside
security-level 100
ip address 10.0.0.111 255.255.255.0
!
interface Port-channel11.101
description INSIDE
vlan 101
nameif inside
security-level 100
ip address 10.1.0.111 255.255.255.0
!
same-security-traffic permit inter-interface
interface TenGigabitEthernet0/6
description CONNECTED_TO_SWITCH-A-VPC
channel-group 11 mode active
no nameif
no security-level
interface TenGigabitEthernet0/7
description CONNECTED_TO_SWITCH-B-VPC
channel-group 11 mode active
no nameif
no security-level
Notes: Interface security levels and traffic filtering parameters are dependent on customer security policies. For the purposes of testing security level 100 is used, and traffic is allowed to traverse between interfaces of the same security level.

## Slide 18
Single VDC (non-FWoS)
Topology
Physical separation of traffic using separate ASA interfaces for Inside and Outside networks.

## Slide 19
ASA1
ASA2
ASA3
ASA4
.111
ITD ‘Single VDC’ Topology
NXOS GBR 7.2 L3 Over VPC
Sw1
DC1-N7K-7
Sw2
DC1-N7K-8
2 Separate VPC trunks
connect to each firewall
.112
.113
.114
SVI VLAN 100 – 10.0.0.17 VRF FW_OUTSIDE
SVI VLAN 101 – 10.1.0.17
SVI VLAN 1100 – 10.100.0.1 (HSRP) VRF FW_OUTSIDE
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interfaces
Outside
Port-Channel 21
VLAN 100
VRF Outside
10.0.0.111 – 114/24
Inside
Port-Channel 11
VLAN 101
10.1.0.111 – 114/24
Firewall Interfaces
NX Transit Interfaces
SVI VLAN 100 – 10.0.0.18
VRF FW_OUTSIDE
Vl101 – 10.1.0.18
NX Transit Interfaces
SVI VLAN 1100 – 10.100.0.1 (HSRP) VRF FW_OUTSIDE
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interfaces
10.0.0.111 Outside
10.1.0.111 Inside
VPC Peer Link
ITD
ITD
Logical View

## Slide 20
ASA1
ASA2
ASA3
ASA4
.111
ITD ‘Single VDC’ Topology
NXOS 6.2.10 – 7.1
Sw1
DC1-N7K-7
Sw2
DC1-N7K-8
.112
.113
.114
SVI VLAN 100 – 10.0.0.17 VRF FW_OUTSIDE
SVI VLAN 101 – 10.1.0.17
SVI VLAN 1100 – 10.100.0.1 (HSRP) VRF FW_OUTSIDE
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interfaces
Outside
TenGigabitEthernet0/6
VLAN 100
VRF Outside
10.0.0.111 – 114/24
Inside
TenGigabitEthernet0/7
VLAN 101
10.1.0.111 – 114/24
Non-VPC port-channels can also be used.
Firewall Interfaces
NX Transit Interfaces
SVI VLAN 100 – 10.0.0.18
VRF FW_OUTSIDE
Vl101 – 10.1.0.18
NX Transit Interfaces
SVI VLAN 1100 – 10.100.0.1 (HSRP) VRF FW_OUTSIDE
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interfaces
VPC Peer Link
ITD
ITD
2 Separate VPC trunks
connect to each firewall
10.0.0.111 Outside
10.1.0.111 Inside
Logical View

## Slide 21
ITD ‘Single VDC’ Topology
Logical View
VLAN 1100
VLAN 100
VLAN 101
VLAN 1101
ITD
ITD
Single VDC
VLAN + VRF Separation
VRF Red – Outside
VRF Blue - Inside

## Slide 22
Nexus 7000
Enable Features
Enable L2 Vlans to be used in the topology
Configure VPC between local and peer switch –Optional
  - Enable L3 Over VPC feature (NXOS 7.2+ only)
Create VRF(s) needed for ITD process
Configure (physical/logical) transit switch interfaces connecting to firewalls Inside and Outside interfaces
Configure ITD Ingress interfaces used to connect to downstream network infrastructure
Define ITD Device Groups and Health Probe parameters
Configure ITD services and mandatory parameters
Configure optional ITD process features
Configuration Steps – Nexus 7000
Configuration steps are shown using NXOS 7.2+ topology

## Slide 23
Enable Features
feature pbr
feature interface-vlan
feature hsrp #optional
feature lacp #optional
feature vpc #optional
feature sla sender
feature sla responder
feature itd
2. Enable L2 Vlans used in topology
vlan 1,100-101,1100-1101
Configuration Steps – Nexus 7000

## Slide 24
  3. Configure VPC between local and peer switch. Enable L3 Over VPC feature (NXOS 7.2+ only) –Optional
vrf context vpc-keepalive
vpc domain 1
peer-keepalive destination 1.1.1.7 source 1.1.1.8 vrf vpc-keepalive
peer-gateway
layer3 peer-router
ipv6 nd synchronize
ip arp synchronize
interface port-channel1
description - VPC PEER LINK
switchport
switchport mode trunk
spanning-tree port type network
vpc peer-link
interface Ethernet1/1
description - VPC KEEP-ALIVE LINK
vrf member vpc-keepalive
ip address 1.1.1.8/24
no shutdown
interface Ethernet1/2-3
description - VPC PEER LINK
switchport
switchport mode trunk
channel-group 1 mode active
no shutdown
Configuration Steps – Nexus 7000

## Slide 25
4. Create VRF(s) needed for ITD process
vrf context FW_OUTSIDE
#In this configuration, Outside traffic heading to the firewall will use the FW_OUTSIDE VRF. After entering and exiting the firewall the traffic will use the default VRF.
#The VRF is needed because L3 interfaces are used to connect to both inside and outside firewall interfaces. VRFs are put in place to prevent traffic from being (inter-vlan) routed “around” the firewall in certain cases.
#Traffic is directed to individual firewalls via PBR, thus routes are not needed.
Configuration Steps – Nexus 7000

## Slide 26
5. Configure (physical/logical) interfaces connecting to firewall Inside and Outside networks
interface Vlan100
description OUTSIDE_FW_VLAN
no shutdown
vrf member FW_OUTSIDE
no ip redirects
ip address 10.0.0.138/24
hsrp 3
ip 10.0.0.100
interface Vlan101
description INSIDE_FW_VLAN
no shutdown
no ip redirects
ip address 10.1.0.18/24
hsrp 1
ip 10.1.0.10
interface Ethernet4/25
description To_ITD-ASA-1_PChannelInside
switchport mode access
switchport access vlan 101
channel-group 11 mode active
interface Ethernet4/26
description To_ITD-ASA-2_PChannelInside
switchport mode access
switchport access vlan 101
channel-group 12 mode active
Configuration Steps – Nexus 7000
interface Ethernet4/1
description To_ITD-ASA-1_PChannelOutside
switchport mode access
switchport access vlan 100
channel-group 21 mode active
interface Ethernet4/2
description To_ITD-ASA-2_PChannelOutside
switchport mode access
switchport access vlan 100
channel group 22 mode active
Replicate for every connecting ASA
interface Port-channel 11
description To_ITD-ASA-1_PChannelInside
switchport mode access
switchport access vlan 101
vpc 11
interface Port-channel 21
description To_ITD-ASA-1_PChannelOutside
switchport mode access
switchport access vlan 100
vpc 21
Replicate for every connecting ASA

## Slide 27
6. Configure ITD Ingress interfaces used to connect to downstream network infrastructure
interface Vlan1100
description EXTERNAL_to_FW-OUTSIDE
vrf member FW_OUTSIDE
no ip redirects
ip address 100.100.0.18/24
hsrp 100
ip 100.100.0.1
interface Vlan1101
description INTERNAL_to_FW-INSIDE
no ip redirects
ip address 10.101.0.18/24
hsrp 1
ip 10.101.0.1
interface port-channel41
description BUNDLE_FOR_AGGREGATE_TRAFFIC
switchport
switchport mode trunk
switchport trunk allowed vlan 1100-1101
vpc 41
interface Ethernet10/1-8
switchport
switchport mode trunk
switchport trunk allowed vlan 1100-1101
channel-group 41
Configuration Steps – Nexus 7000

## Slide 28
7. Define ITD Device Groups and Health Probe parameters
itd device-group FW_INSIDE
#Config Firewall Inside interfaces as nodes
node ip 10.1.0.111
node ip 10.1.0.112
node ip 10.1.0.113
node ip 10.1.0.114
probe icmp frequency 5 timeout 5 retry-count 1
itd device-group FW_OUTSIDE
#Config Firewall Outside interfaces as nodes
node ip 10.0.0.111
node ip 10.0.0.112
node ip 10.0.0.113
node ip 10.0.0.114
probe icmp frequency 5 timeout 5 retry-count 1
Probe Default Values switch(config-device-group)# probe icmp frequency 10 retry-down-count 1 retry-up-count 1 timeout 5
Configuration Steps – Nexus 7000

## Slide 29
8. Configure Mandatory ITD Service Processes
itd INSIDE
device-group FW_INSIDE
#binds inside firewall interfaces to process
ingress interface Vlan1101
#applies ITD route-map to Vlan1101 interface
failaction node reassign
#dictates to use the next available Active FW if a FW goes offline
load-balance method src ip
#distributes traffic into 16 buckets
#load balances traffic applicable in buckets to firewalls based on source-IP address (default).
no shut
itd OUTSIDE
vrf FW_OUTSIDE
#applies this ITD process to the defined vrf named ‘FW_OUTSIDE’
device-group FW_OUTSIDE
ingress interface Vlan1100
failaction node reassign
load-balance method dst ip
#load balances traffic applicable in buckets to firewalls based on destination. Default is src-ip (itd INSIDE)
no shut
Configuration Steps – Nexus 7000

## Slide 30
10. Configure optional ITD features
N7K-1(config)# itd INSIDE
N7K-1(config-itd)# ?
access-list ITD access-list name ##Traffic to include in LB Profile
device-group ITD device group
exclude ACL to exclude from redirection ##Traffic to exclude from LB Profile
failaction ITD failaction
ingress ITD ingress interface
load-balance ITD Loadbalance ##Configures bucket allocation, mask position, or Src/Dst LB Method
nat Network Address Translation ##Enables NAT Based ITD instead of PBR based (default)
no Negate a command or set its defaults
peer Peer cli for sandwich mode failure notification ##Enables awareness of ITD process state in another VDC (used for 2-Arm/Sandwich ITD configurations)
shutdown
virtual ITD virtual ip configuration ##Global and Device-group specific VIP configuration
vrf ITD service vrf
Configuration Steps – Nexus 7000

## Slide 31
Configuration Steps – ASA Firewall
ASA Basic Configuration: There is nothing ITD specific about configuring the ASA for ITD. The following interface configuration is used with this topology.
interface Port-channel11
description INSIDE
vlan 101
nameif inside
security-level 100
ip address 10.1.0.111 255.255.255.0
!
interface Port-channel21
description OUTSIDE
vlan 100
nameif outside
security-level 100
ip address 10.0.0.111 255.255.255.0
!
same-security-traffic permit inter-interface
interface TenGigabitEthernet0/6
description CONNECTED_TO_SWITCH-A-VPC
channel-group 11 mode active
no nameif
no security-level
interface TenGigabitEthernet0/7
description CONNECTED_TO_SWITCH-B-VPC
channel-group 11 mode active
no nameif
no security-level
interface TenGigabitEthernet0/8
description CONNECTED_TO_SWITCH-A-VPC
channel-group 21 mode active
no nameif
no security-level
interface TenGigabitEthernet0/9
description CONNECTED_TO_SWITCH-B-VPC
channel-group 21 mode active
no nameif
no security-level
Notes: Interface security levels and traffic filtering parameters are dependent on customer security policies. For the purposes of testing security level 100 is used, and traffic is allowed to traverse between interfaces of the same security level.

## Slide 32
ITD + ASA with dual VDC
Sandwich Topology
Physical separation of traffic using separate ASA interfaces for Inside and Outside networks.

## Slide 33
ASA1
ASA2
ASA3
ASA4
.111
Dual VDC Sandwich Topology
NXOS GBR 7.2 L3 Over VPC
.112
.113
.114
SVI VLAN 100 – 10.0.0.17 VRF FW_OUTSIDE
SVI VLAN 101 – 10.1.0.17
Outside
Port-Channel 21
VLAN 100
VRF Outside
10.0.0.111 – 114/24
Inside
Port-Channel 11
VLAN 101
10.1.0.111 – 114/24
Firewall Interfaces
NX Transit Interfaces
SVI VLAN 1100 – 10.100.0.1 VRF FW_OUTSIDE
NX ITD Ingress Interfaces
10.0.0.114 Outside
10.1.0.114 Inside
ITD
ITD
SVI VLAN 1101 – 10.101.0.1
NX ITD Ingress Interface
VDC 2
VDC 1

## Slide 34
Nexus 7000
Create VDC and allocate ports (not displayed)
Enable Features
Enable L2 Vlans to be used in the topology
Configure (physical/logical) interfaces connecting to firewalls Inside and Outside networks
Configure transit interfaces used for getting internal traffic flow to firewall
Define ITD Device Groups and Health Probe parameters
Configure ITD services and mandatory parameters
Configure optional ITD parameters
Configuration Steps – Nexus 7000
All configuration steps are done in each VDC (or individual switch on each side of the “sandwich” configuration.

## Slide 35
Create VDC and allocate ports (not shown)
Enable Features
feature pbr
feature interface-vlan
feature sla sender
feature sla responder
feature itd
3. Enable L2 Vlans used in topology
#VDC 1 - Inside
Vlan 101,1101
Configuration Steps – Nexus 7000
#VDC 2 – Outside
Vlan 100,1001

## Slide 36
4. Configure (physical/logical) interfaces connecting to firewall Inside and Outside networks
#VDC1
interface Vlan101
description INSIDE_FW_VLAN
no ip redirects
ip address 10.1.0.18/24
no shutdown
interface Ethernet4/25
description To_ITD-ASA-1_Intf_Te0/6
switchport mode access
switchport access vlan 101
no shutdown
#VDC2
interface Vlan100
description OUTSIDE_FW_VLAN
no ip redirects
ip address 10.0.0.138/24
no shutdown
interface Ethernet4/1
description To_ITD-ASA-1_Intf_Te0/8
switchport mode access
switchport access vlan 100
no shutdown
Configuration Steps – Nexus 7000
interface Ethernet4/26
description To_ITD-ASA-2_Intf_Te0/6
switchport mode access
switchport access vlan 101
no shutdown
interface Ethernet4/28
description To_ITD-ASA-4_Intf_Te0/6
switchport mode access
switchport access vlan 101
no shutdown
interface Ethernet4/2
description To_ITD-ASA-2_Intf_Te0/8
switchport mode access
switchport access vlan 100
no shutdown
interface Ethernet4/4
description To_ITD-ASA-4_Intf_Te0/8
switchport mode access
switchport access vlan 100
no shutdown
interface Ethernet4/27
description To_ITD-ASA-3_Intf_Te0/6
switchport mode access
switchport access vlan 101
no shutdown
interface Ethernet4/3
description To_ITD-ASA-3_Intf_Te0/8
switchport mode access
switchport access vlan 100
no shutdown

## Slide 37
5. Configure transit interfaces used for getting internal traffic flow to firewall
#VDC2
interface Vlan1001
description EXTERNAL_to_FW-OUTSIDE
no ip redirects
ip address 10.100.0.138/24
no shutdown
Configuration Steps – Nexus 7000
interface Ethernet10/13-20
description “connection to Breaking Point”
switchport
switchport mode access
switchport access vlan 1001
no shutdown
#VDC1
interface Vlan1101
description INTERNAL_to_FW-INSIDE
no ip redirects
ip address 10.101.0.18/24
no shutdown
interface Ethernet10/1-8
description “connection to Breaking Point”
switchport
switchport mode access
switchport access vlan 1101
no shutdown

## Slide 38
6. Define ITD Device Groups and Health Probe parameters
#VDC1
itd device-group FW_INSIDE
#Config Firewall Inside interfaces as nodes
node ip 10.1.0.111
node ip 10.1.0.112
node ip 10.1.0.113
node ip 10.1.0.114
probe icmp frequency 5 timeout 5 retry-count 1
#VDC2
itd device-group FW_OUTSIDE
#Config Firewall Outside interfaces as nodes
node ip 10.0.0.111
node ip 10.0.0.112
node ip 10.0.0.113
node ip 10.0.0.114
probe icmp frequency 5 timeout 5 retry-count 1
Probe Default Values switch(config-device-group)# probe icmp frequency 10 retry-down-count 1 retry-up-count 1 timeout 5
Configuration Steps – Nexus 7000

## Slide 39
7. Configure Mandatory ITD Service Processes
itd INSIDE
device-group FW_INSIDE
#binds inside firewall interfaces to process
ingress interface Vlan1101
#applies ITD route-map to Vlan1101 interface
failaction node reassign
#dictates to use the next available Active FW if a FW goes offline
load-balance method src ip
#distributes traffic into 16 buckets
#load balances traffic applicable in buckets to firewalls based on source-IP address (default).
peer vdc VDC2
#enables awareness of ITD process in peer VDC for sandwich mode. If a device is connected to both VDCs (2 arm) and all links of the arm connected to the peer fails, then locally connected links will also be disabled to prevent blackholing of traffic.
no shut
itd OUTSIDE
device-group FW_OUTSIDE
ingress interface Vlan1100
failaction node reassign
load-balance method dst ip
#load balances traffic applicable in buckets to firewalls based on destination. Default is src-ip (itd INSIDE)
peer vdc VDC1
no shut
Configuration Steps – Nexus 7000

## Slide 40
8. Configure optional ITD features
N7K-1(config)# itd INSIDE
N7K-1(config-itd)# ?
access-list ITD access-list name ##Traffic to include in LB Profile
device-group ITD device group
exclude ACL to exclude from redirection ##Traffic to exclude from LB Profile
failaction ITD failaction
ingress ITD ingress interface
load-balance ITD Loadbalance ##Configures bucket allocation, mask position, or Src/Dst LB Method
nat Network Address Translation ##Enables NAT Based ITD instead of PBR based (default)
no Negate a command or set its defaults
peer Peer cli for sandwich mode failure notification ##Enables awareness of ITD process state in another VDC (used for 2-Arm/Sandwich ITD configurations)
shutdown
virtual ITD virtual ip configuration ##Global and Device-group specific VIP configuration
vrf ITD service vrf #applies this ITD process to a defined vrf
Configuration Steps – Nexus 7000

## Slide 41
Configuration Steps – ASA Firewall
ASA Basic Configuration: There is nothing ITD specific about configuring the ASA for ITD. The following interface configuration is used with this topology.
!
interface TenGigabitEthernet0/6
description INSIDE
nameif inside
security-level 100
ip address 10.1.0.111 255.255.255.0
!
!
interface TenGigabitEthernet0/8
description OUTSIDE
nameif outside
security-level 100
ip address 10.0.0.111 255.255.255.0
!
INSIDE and OUTSIDE interface configuration on ASA
Repeat on each ASA-1, ASA-2, ASA-3, ASA-4
Configure different IP address for INSIDE and OUTSIDE interface on all Firewalls.
Note: If security levels are the same for inside and outside interfaces, ‘same-security-traffic permit’ command can be configured.
If varying security levels are used, ensure appropriate ACLs are configured.
Notes: Interface security levels and traffic filtering parameters are dependent on customer security policies. For the purposes of testing security level 100 is used, and traffic is allowed to traverse between interfaces of the same security level.

## Slide 42
ITD +ASA with dual VDC + vPC
Sandwich Topology
Physical separation of traffic using separate ASA interfaces for Inside and Outside networks.

## Slide 43
VPC + Dual VDC Sandwich Topology
NXOS GBR 7.2 L3 Over VPC
SVI VLAN 100 – 10.0.0.17 VRF FW_OUTSIDE
SVI VLAN 101 – 10.1.0.17
Outside
Port-Channel 21
VLAN 100
VRF Outside
10.0.0.111 – 114/24
Inside
Port-Channel 11
VLAN 101
10.1.0.111 – 114/24
Firewall Interfaces
NX Transit Interfaces
SVI VLAN 100 – 10.0.0.18
VRF FW_OUTSIDE
Vl101 – 10.1.0.18
NX Transit Interfaces
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interface
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interface
ASA1
ASA2
ASA3
ASA4
.111
Sw1
DC1-N7K-7
Sw2
DC1-N7K-8
.112
.113
.114
SVI VLAN 1100 – 10.100.0.1 (HSRP) VRF FW_OUTSIDE
NX ITD Ingress Interfaces
VPC Peer Link
ITD
ITD
Sw1
DC1-N7K-7
Sw2
DC1-N7K-8
VPC Peer Link
ITD
ITD
VDC 2
VDC 1
VDC 1
VDC 2

## Slide 44
SVI VLAN 100 – 10.0.0.17 VRF FW_OUTSIDE
SVI VLAN 101 – 10.1.0.17
NX Transit Interfaces
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interface
Outside
Port-Channel 21
VLAN 100
VRF Outside
10.0.0.111 – 114/24
Inside
Port-Channel 11
VLAN 101
10.1.0.111 – 114/24
Firewall Interfaces
SVI VLAN 100 – 10.0.0.18
VRF FW_OUTSIDE
Vl101 – 10.1.0.18
NX Transit Interfaces
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interface
VPC + Dual VDC Sandwich Topology
NXOS 6.2.10 – 7.1
ASA1
ASA2
ASA3
ASA4
.111
Sw1
DC1-N7K-7
Sw2
DC1-N7K-8
.112
.113
.114
VPC Peer Link
ITD
ITD
Sw1
DC1-N7K-7
Sw2
DC1-N7K-8
VPC Peer Link
ITD
ITD
VDC 2
VDC 1
VDC 1
VDC 2
SVI VLAN 1100 – 10.100.0.1 (HSRP) VRF FW_OUTSIDE
NX ITD Ingress Interfaces

## Slide 45
Nexus 7000
Create VDC and allocate ports (not displayed)
Enable Features
Enable L2 Vlans to be used in the topology
Configure VPC between local and peer switch –Optional
  - Enable L3 Over VPC feature (NXOS 7.2+ only)
Create VRF(s) needed for ITD process –Optional
Configure (physical/logical) transit switch interfaces connecting to firewalls Inside and Outside interfaces
Configure ITD Ingress interfaces that connect to downstream network infrastructure
Define ITD Device Groups and Health Probe parameters
Configure ITD service and mandatory parameters
Enabled optional ITD features
Configuration Steps – Nexus 7000
All configuration steps are done in each VDC (or individual switch on each side of the “sandwich” configuration. Configuration steps are shown using NXOS 7.2+ topology.

## Slide 46
Create VDC and allocate ports (not shown)
Enable Features
feature pbr
feature interface-vlan
feature hsrp #optional
feature lacp #optional
feature vpc
feature sla sender
feature sla responder
feature itd
3. Enable L2 Vlans used in topology
#VDC 1 - Inside
Vlan 101,1101
Configuration Steps – Nexus 7000
#VDC 2 – Outside
Vlan 100,1100

## Slide 47
  Configure VPC between local and peer switch. Enable L3 Over VPC feature (NXOS 7.2+ only) –Optional
#VDC1 – Inside
vrf context vpc-keepalive
vpc domain 1
peer-keepalive destination 1.1.1.7 source 1.1.1.8 vrf vpc-keepalive
peer-gateway
layer3 peer-router
ipv6 nd synchronize
ip arp synchronize
interface port-channel1
description - VPC PEER LINK
switchport
switchport mode trunk
spanning-tree port type network
vpc peer-link
interface Ethernet1/1
description - VPC KEEP-ALIVE LINK
vrf member vpc-keepalive
ip address 1.1.1.8/24
interface Ethernet1/2-3
description - VPC PEER LINK
switchport
switchport mode trunk
channel-group 1 mode active
Configuration Steps – Nexus 7000

## Slide 48
#VDC2 – Outside
vrf context vpc-keepalive
vpc domain 1
peer-keepalive destination 2.2.2.7 source 2.2.2.8 vrf vpc-keepalive
peer-gateway
layer3 peer-router
ipv6 nd synchronize
ip arp synchronize
interface port-channel1
description - VPC PEER LINK
switchport
switchport mode trunk
spanning-tree port type network
vpc peer-link
interface Ethernet1/1
description - VPC KEEP-ALIVE LINK
vrf member vpc-keepalive
ip address 2.2.2.8/24
no shutdown
interface Ethernet1/2-3
description - VPC PEER LINK
switchport
switchport mode trunk
channel-group 1 mode active
no shutdown
Configuration Steps – Nexus 7000
4. Cont. –Optional

## Slide 49
5. Create VRF(s) needed for ITD process –Optional
Configuration Steps – Nexus 7000
Since VDCs segment traffic, additional VRFs are not needed

## Slide 50
6. Configure (physical/logical) interfaces connecting to firewall Inside and Outside networks
#VDC1
interface Vlan101
description INSIDE_FW_VLAN
no shutdown
no ip redirects
ip address 10.1.0.18/24
hsrp 1
ip 10.1.0.10
interface Ethernet4/25
description To_ITD-ASA-1_Po11-VPC
switchport mode access
switchport access vlan 101
channel-group 11 mode active
interface Ethernet4/26
description To_ITD-ASA-2_Po12-VPC
switchport mode access
switchport access vlan 101
channel-group 12 mode active
interface Ethernet4/27
description To_ITD-ASA-3_Po13-VPC
switchport mode access
switchport access vlan 101
channel-group 13 mode active
Replicate for every connecting ASA
Configuration Steps – Nexus 7000
interface Port-channel 11
description To_ITD-ASA-1_PChannelInside
switchport mode access
switchport access vlan 101
vpc 11
interface Port-channel 12
description To_ITD-ASA-2_PChannelInside
switchport mode access
switchport access vlan 101
vpc 12
interface Port-channel 13
description To_ITD-ASA-3_PChannelInside
switchport mode access
switchport access vlan 101
vpc 13
interface Port-channel 14
description To_ITD-ASA-4_PChannelInside
switchport mode access
switchport access vlan 101
vpc 14
Replicate for every connecting ASA

## Slide 51
6. Cont. (VDC #2 – Outside)
#VDC2
interface Vlan100
description OUTSIDE_FW_VLAN
no shutdown
no ip redirects
ip address 10.0.0.138/24
hsrp 3
ip 10.0.0.100
interface Ethernet4/1
description To_ITD-ASA-1_Po21-VPC
switchport mode access
switchport access vlan 100
no shutdown
interface Ethernet4/2
description To_ITD-ASA-2_Po22-VPC
switchport mode access
switchport access vlan 100
no shutdown
interface Ethernet4/3
description To_ITD-ASA-3_Po23-VPC
switchport mode access
switchport access vlan 100
no shutdown
Replicate for every connecting ASA
Configuration Steps – Nexus 7000
interface Port-channel 21
description To_ITD-ASA-1_PChannelOutside
switchport mode access
switchport access vlan 100
vpc 21
interface Port-channel 22
description To_ITD-ASA-2_PChannelOutside
switchport mode access
switchport access vlan 100
vpc 22
interface Port-channel 23
description To_ITD-ASA-3_PChannelOutside
switchport mode access
switchport access vlan 100
vpc 23
interface Port-channel 24
description To_ITD-ASA-4_PChannelOutside
switchport mode access
switchport access vlan 100
vpc 24
Replicate for every connecting ASA

## Slide 52
7. Configure transit interfaces used for getting internal traffic flow to firewall
#VDC2
interface Vlan1001
description EXTERNAL_to_FW-OUTSIDE
no shutdown
no ip redirects
ip address 10.100.0.138/24
hsrp 100
ip 10.100.0.1
Configuration Steps – Nexus 7000
interface port-channel42
description BUNDLE_FOR_AGGREGATE_TRAFFIC
switchport
switchport mode access
switchport access vlan 1001
vpc 42
interface Ethernet10/13-20
switchport
switchport mode access
switchport access vlan 1001
channel-group 42
no shutdown
#VDC1
interface Vlan1101
description INTERNAL_to_FW-INSIDE
no shutdown
no ip redirects
ip address 10.101.0.18/24
hsrp 1
ip 10.101.0.1
interface port-channel41
description BUNDLE_FOR_AGGREGATE_TRAFFIC
switchport
switchport mode access
switchport access vlan 1101
vpc 41
interface Ethernet10/1-8
switchport
switchport mode access
switchport access vlan 1101
channel-group 41
no shutdown

## Slide 53
8. Define ITD Device Groups and Health Probe parameters
#VDC1
itd device-group FW_INSIDE
#Config Firewall Inside interfaces as nodes
node ip 10.1.0.111
node ip 10.1.0.112
node ip 10.1.0.113
node ip 10.1.0.114
probe icmp frequency 5 timeout 5 retry-count 1
#VDC2
itd device-group FW_OUTSIDE
#Config Firewall Outside interfaces as nodes
node ip 10.0.0.111
node ip 10.0.0.112
node ip 10.0.0.113
node ip 10.0.0.114
probe icmp frequency 5 timeout 5 retry-count 1
Probe Default Values switch(config-device-group)# probe icmp frequency 10 retry-down-count 1 retry-up-count 1 timeout 5
Configuration Steps – Nexus 7000

## Slide 54
9. Configure Mandatory ITD Service Processes
#VDC1
itd INSIDE
device-group FW_INSIDE
#binds inside firewall interfaces to process
ingress interface Vlan1101
#applies ITD route-map to Vlan1101 interface
failaction node reassign
#dictates to use the next available Active FW if a FW goes offline
load-balance method src ip
#distributes traffic into 16 buckets
#load balances traffic applicable in buckets to firewalls based on source-IP address (default).
peer vdc VDC2
#enables awareness of ITD process in peer VDC for sandwich mode. If a device is connected to both VDCs (2 arm) and all links of the arm connected to the peer fails, then locally connected links will also be disabled to prevent blackholing of traffic.
no shut
#VDC2
itd OUTSIDE
device-group FW_OUTSIDE
ingress interface Vlan1100
failaction node reassign
load-balance method dst ip
#load balances traffic applicable in buckets to firewalls based on destination. Default is src-ip (itd INSIDE)
peer vdc VDC1
no shut
Configuration Steps – Nexus 7000

## Slide 55
10. Configure optional ITD features
N7K-1(config)# itd INSIDE
N7K-1(config-itd)# ?
access-list ITD access-list name ##Traffic to include in LB Profile
device-group ITD device group
exclude ACL to exclude from redirection ##Traffic to exclude from LB Profile
failaction ITD failaction
ingress ITD ingress interface
load-balance ITD Loadbalance ##Configures bucket allocation, mask position, or Src/Dst LB Method
nat Network Address Translation ##Enables NAT Based ITD instead of PBR based (default)
no Negate a command or set its defaults
peer Peer cli for sandwich mode failure notification ##Enables awareness of ITD process state in another VDC (used for 2-Arm/Sandwich ITD configurations)
shutdown
virtual ITD virtual ip configuration ##Global and Device-group specific VIP configuration
vrf ITD service vrf
Configuration Steps – Nexus 7000

## Slide 56
Configuration Steps – ASA Firewall
ASA Basic Configuration: There is nothing ITD specific about configuring the ASA for ITD. The following interface configuration is used with this topology.
!
interface TenGigabitEthernet0/6
description INSIDE
nameif inside
security-level 100
ip address 10.1.0.111 255.255.255.0
!
!
interface TenGigabitEthernet0/8
description OUTSIDE
nameif outside
security-level 100
ip address 10.0.0.111 255.255.255.0
!
same-security-traffic permit inter-interface
INSIDE and OUTSIDE interface configuration on ASA
Repeat on each ASA-1, ASA-2, ASA-3, ASA-4
Configure different IP address for INSIDE and OUTSIDE interface on all Firewalls.
Note: If security levels are the same for inside and outside interfaces, ‘same-security-traffic permit’ command can be configured.
If varying security levels are used, ensure appropriate ACLs are configured.
Notes: Interface security levels and traffic filtering parameters are dependent on customer security policies. For the purposes of testing security level 100 is used, and traffic is allowed to traverse between interfaces of the same security level.

## Slide 57
ITD +ASA Cluster with dual VDC + vPC
Sandwich Topology
Physical separation of traffic using separate ASA interfaces for Inside and Outside networks.

## Slide 58
ASA1
ASA2
ASA3
ASA4
.111
L3 Cluster + VPC + Dual VDC Sandwich
NXOS GBR 7.2 L3 Over VPC
Sw1
DC1-N7K-7
Sw2
DC1-N7K-8
.112
.113
.114
SVI VLAN 100 – 10.0.0.17 VRF FW_OUTSIDE
SVI VLAN 101 – 10.1.0.17
Outside
Port-Channel 21
VLAN 100
VRF Outside
10.0.0.111 – 114/24
Inside
Port-Channel 11
VLAN 101
10.1.0.111 – 114/24
Firewall Interfaces
NX Transit Interfaces
SVI VLAN 100 – 10.0.0.18
VRF FW_OUTSIDE
Vl101 – 10.1.0.18
NX Transit Interfaces
SVI VLAN 1100 – 10.100.0.1 (HSRP) VRF FW_OUTSIDE
NX ITD Ingress Interfaces
VPC Peer Link
ITD
ITD
Sw1
DC1-N7K-7
Sw2
DC1-N7K-8
VPC Peer Link
ITD
ITD
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interface
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interface
VDC 2
VDC 1
VDC 1
VDC 2
CCL
Individual Mode ASA Cluster
L3 Routed Firewalls
Each cluster member has its own unique IP allocated from a cluster pool, maintains its own ARP and Routing Tables
Each firewall has its own port-channel to connect the VPC peers.

## Slide 59
ASA1
ASA2
ASA3
ASA4
.111
Sw1
DC1-N7K-7
Sw2
DC1-N7K-8
.112
.113
.114
VPC Peer Link
ITD
ITD
Sw1
DC1-N7K-7
Sw2
DC1-N7K-8
VPC Peer Link
ITD
ITD
VDC 2
VDC 1
VDC 1
VDC 2
SVI VLAN 100 – 10.0.0.17 VRF FW_OUTSIDE
SVI VLAN 101 – 10.1.0.17
NX Transit Interfaces
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interface
Outside
Port-Channel 21
VLAN 100
VRF Outside
10.0.0.111 – 114/24
Inside
Port-Channel 11
VLAN 101
10.1.0.111 – 114/24
Firewall Interfaces
SVI VLAN 100 – 10.0.0.18
VRF FW_OUTSIDE
Vl101 – 10.1.0.18
NX Transit Interfaces
SVI VLAN 1101 – 10.101.0.1 (HSRP)
NX ITD Ingress Interface
L3 Cluster + VPC + Dual VDC Sandwich
NXOS 6.2.10 – 7.1
SVI VLAN 1100 – 10.100.0.1 (HSRP) VRF FW_OUTSIDE
NX ITD Ingress Interfaces
CCL
Individual Mode ASA Cluster
L3 Routed Firewalls
Each cluster member has its own unique IP allocated from a cluster pool, maintains its own ARP and Routing Tables
Each firewall has its own port-channel to connect to 1 of the VPC peers. A single non-VPC firewall interface (e.g., te0/6) can also be used.

## Slide 60
Nexus 7000
Create VDC and allocate ports (not displayed)
Enable Features
Enable L2 Vlans to be used in the topology
Configure VPC between local and peer switch
  - Enable L3 Over VPC feature (NXOS 7.2+ only)
Create VRF(s) needed for ITD process –Optional
Configure (physical/logical) transit switch interfaces connecting to firewalls Inside and Outside interfaces
Configure ITD Ingress interfaces that connect to downstream network infrastructure
Define ITD Device Groups and Health Probe parameters
Configure ITD service and mandatory parameters
Enabled optional ITD features
Configuration Steps – Nexus 7000
All configuration steps are done in each VDC (or individual switch on each side of the “sandwich” configuration. Configuration steps are shown using NXOS 7.2+ topology.

## Slide 61
Create VDC and allocate ports (not shown)
Enable Features
feature pbr
feature interface-vlan
feature hsrp #optional
feature lacp #optional
feature vpc #optional
feature sla sender
feature sla responder
feature itd
3. Enable L2 Vlans used in topology
#VDC 1 - Inside
Vlan 101,1101
Configuration Steps – Nexus 7000
#VDC 2 – Outside
Vlan 100,1100

## Slide 62
  Configure VPC between local and peer switch. Enable L3 Over VPC feature (NXOS 7.2+ only)
#VDC1 – Inside
vrf context vpc-keepalive
vpc domain 1
peer-keepalive destination 1.1.1.7 source 1.1.1.8 vrf vpc-keepalive
peer-gateway
layer3 peer-router
ipv6 nd synchronize
ip arp synchronize
interface port-channel1
description - VPC PEER LINK
switchport
switchport mode trunk
spanning-tree port type network
vpc peer-link
interface Ethernet1/1
description - VPC KEEP-ALIVE LINK
vrf member vpc-keepalive
ip address 1.1.1.8/24
interface Ethernet1/2-3
description - VPC PEER LINK
switchport
switchport mode trunk
channel-group 1 mode active
Configuration Steps – Nexus 7000

## Slide 63
#VDC2 – Outside
vrf context vpc-keepalive
vpc domain 1
peer-keepalive destination 2.2.2.7 source 2.2.2.8 vrf vpc-keepalive
peer-gateway
layer3 peer-router
ipv6 nd synchronize
ip arp synchronize
interface port-channel1
description - VPC PEER LINK
switchport
switchport mode trunk
spanning-tree port type network
vpc peer-link
interface Ethernet1/1
description - VPC KEEP-ALIVE LINK
vrf member vpc-keepalive
ip address 2.2.2.8/24
no shutdown
interface Ethernet1/2-3
description - VPC PEER LINK
switchport
switchport mode trunk
channel-group 1 mode active
no shutdown
Configuration Steps – Nexus 7000
4. Cont.

## Slide 64
5. Create VRF(s) needed for ITD process –Optional
Configuration Steps – Nexus 7000
Since VDCs segment traffic, additional VRFs are not needed

## Slide 65
6. Configure (physical/logical) interfaces connecting to firewall Inside and Outside networks
#VDC1
interface Vlan101
description INSIDE_FW_VLAN
no shutdown
no ip redirects
ip address 10.1.0.18/24
hsrp 1
ip 10.1.0.10
interface Ethernet4/25
description To_ITD-ASA-1_Po11-VPC
switchport mode access
switchport access vlan 101
channel-group 11 mode active
interface Ethernet4/26
description To_ITD-ASA-2_Po12-VPC
switchport mode access
switchport access vlan 101
channel-group 12 mode active
interface Ethernet4/27
description To_ITD-ASA-3_Po13-VPC
switchport mode access
switchport access vlan 101
channel-group 13 mode active
Replicate for every connecting ASA
Configuration Steps – Nexus 7000
interface Port-channel 11
description To_ITD-ASA-1_PChannelInside
switchport mode access
switchport access vlan 101
vpc 11
interface Port-channel 12
description To_ITD-ASA-2_PChannelInside
switchport mode access
switchport access vlan 101
vpc 12
interface Port-channel 13
description To_ITD-ASA-3_PChannelInside
switchport mode access
switchport access vlan 101
vpc 13
interface Port-channel 14
description To_ITD-ASA-4_PChannelInside
switchport mode access
switchport access vlan 101
vpc 14
Replicate for every connecting ASA

## Slide 66
6. Cont. (VDC #2 – Outside)
#VDC2
interface Vlan100
description OUTSIDE_FW_VLAN
no shutdown
no ip redirects
ip address 10.0.0.138/24
hsrp 3
ip 10.0.0.100
interface Ethernet4/1
description To_ITD-ASA-1_Po21-VPC
switchport mode access
switchport access vlan 100
no shutdown
interface Ethernet4/2
description To_ITD-ASA-2_Po22-VPC
switchport mode access
switchport access vlan 100
no shutdown
interface Ethernet4/3
description To_ITD-ASA-3_Po23-VPC
switchport mode access
switchport access vlan 100
no shutdown
Replicate for every connecting ASA
Configuration Steps – Nexus 7000
interface Port-channel 21
description To_ITD-ASA-1_PChannelOutside
switchport mode access
switchport access vlan 100
vpc 21
interface Port-channel 22
description To_ITD-ASA-2_PChannelOutside
switchport mode access
switchport access vlan 100
vpc 22
interface Port-channel 23
description To_ITD-ASA-3_PChannelOutside
switchport mode access
switchport access vlan 100
vpc 23
interface Port-channel 24
description To_ITD-ASA-4_PChannelOutside
switchport mode access
switchport access vlan 100
vpc 24
Replicate for every connecting ASA

## Slide 67
7. Configure ITD Ingress interfaces that connect to downstream network infrastructure
#VDC2
interface Vlan1001
description EXTERNAL_to_FW-OUTSIDE
no shutdown
no ip redirects
ip address 10.100.0.138/24
hsrp 100
ip 10.100.0.1
Configuration Steps – Nexus 7000
interface port-channel42
description BUNDLE_FOR_AGGREGATE_TRAFFIC
switchport
switchport mode access
switchport access vlan 1001
vpc 42
interface Ethernet10/13-20
switchport
switchport mode access
switchport access vlan 1001
channel-group 42
no shutdown
#VDC1
interface Vlan1101
description INTERNAL_to_FW-INSIDE
no shutdown
no ip redirects
ip address 10.101.0.18/24
hsrp 1
ip 10.101.0.1
interface port-channel41
description BUNDLE_FOR_AGGREGATE_TRAFFIC
switchport
switchport mode access
switchport access vlan 1101
vpc 41
interface Ethernet10/1-8
switchport
switchport mode access
switchport access vlan 1101
channel-group 41
no shutdown

## Slide 68
8. Define ITD Device Groups and Health Probe parameters
#VDC1
itd device-group FW_INSIDE
#Config Firewall Inside interfaces as nodes
node ip 10.1.0.111
node ip 10.1.0.112
node ip 10.1.0.113
node ip 10.1.0.114
probe icmp frequency 5 timeout 5 retry-count 1
#VDC2
itd device-group FW_OUTSIDE
#Config Firewall Outside interfaces as nodes
node ip 10.0.0.111
node ip 10.0.0.112
node ip 10.0.0.113
node ip 10.0.0.114
probe icmp frequency 5 timeout 5 retry-count 1
Probe Default Values switch(config-device-group)# probe icmp frequency 10 retry-down-count 1 retry-up-count 1 timeout 5
Configuration Steps – Nexus 7000

## Slide 69
9. Configure Mandatory ITD Service Processes
#VDC1
itd INSIDE
device-group FW_INSIDE
#binds inside firewall interfaces to process
ingress interface Vlan1101
#applies ITD route-map to Vlan1101 interface
failaction node reassign
#dictates to use the next available Active FW if a FW goes offline
load-balance method src ip
#distributes traffic into 16 buckets
#load balances traffic applicable in buckets to firewalls based on source-IP address (default).
peer vdc VDC2
#enables awareness of ITD process in peer VDC for sandwich mode. If a device is connected to both VDCs (2 arm) and all links of the arm connected to the peer fails, then locally connected links will also be disabled to prevent blackholing of traffic.
no shut
#VDC2
itd OUTSIDE
device-group FW_OUTSIDE
ingress interface Vlan1100
failaction node reassign
load-balance method dst ip
#load balances traffic applicable in buckets to firewalls based on destination. Default is src-ip (itd INSIDE)
peer vdc VDC1
no shut
Configuration Steps – Nexus 7000

## Slide 70
10. Configure optional ITD features
N7K-1(config)# itd INSIDE
N7K-1(config-itd)# ?
access-list ITD access-list name ##Traffic to include in LB Profile
device-group ITD device group
exclude ACL to exclude from redirection ##Traffic to exclude from LB Profile
failaction ITD failaction
ingress ITD ingress interface
load-balance ITD Loadbalance ##Configures bucket allocation, mask position, or Src/Dst LB Method
nat Network Address Translation ##Enables NAT Based ITD instead of PBR based (default)
no Negate a command or set its defaults
peer Peer cli for sandwich mode failure notification ##Enables awareness of ITD process state in another VDC (used for 2-Arm/Sandwich ITD configurations)
shutdown
virtual ITD virtual ip configuration ##Global and Device-group specific VIP configuration
vrf ITD service vrf #applies this ITD process to the defined vrf
Configuration Steps – Nexus 7000

## Slide 71
Configuration Steps – ASA Firewall
ASA Basic Configuration: There is nothing ITD specific about configuring the ASA L3 Cluster for ITD. The following interface configuration is used with this topology. Follow ASA Configuration Guide for full configuration instructions.
http://www.cisco.com/c/en/us/td/docs/security/asa/asa90/configuration/guide/asa_90_cli_config/ha_cluster.html
cluster group ASA-CLUSTER-L3
local-unit ASA1
cluster-interface Port-channel31 ip 10.2.0.1 255.255.255.0
priority 1
health-check holdtime 1.5
clacp system-mac auto system-priority 1
enable
mac-address pool MAC-INSIDE aaaa.0101.0001 - aaaa.0101.0008
mac-address pool MAC-OUTSIDE aaaa.0100.0001 - aaaa.0100.0008
ip local pool IP-OUTSIDE 10.0.0.111-10.0.0.114
ip local pool IP-INSIDE 10.1.0.111-10.1.0.114
interface Port-channel11
description INSIDE
lacp max-bundle 8
mac-address cluster-pool MAC-INSIDE
nameif inside
security-level 100
ip address 10.1.0.11 255.255.255.0 cluster-pool IP-INSIDE
!
interface Port-channel21
description OUTSIDE
lacp max-bundle 8
mac-address cluster-pool MAC-OUTSIDE
nameif outside
security-level 100
ip address 10.0.0.11 255.255.255.0 cluster-pool IP-OUTSIDE
interface Port-channel31
description Clustering Interface
lacp max-bundle 8
!
interface TenGigabitEthernet0/6
channel-group 11 mode active
no nameif
no security-level
no ip address
!
interface TenGigabitEthernet0/7
channel-group 11 mode active
no nameif
no security-level
no ip address
!
interface TenGigabitEthernet0/8
channel-group 21 mode active
no nameif
no security-level
no ip address
!
interface TenGigabitEthernet0/9
description OUTSIDE
channel-group 21 mode active
no nameif
no security-level
no ip address
!
interface TenGigabitEthernet1/0
channel-group 31 mode on
no nameif
no security-level
no ip address
!
interface TenGigabitEthernet1/1
channel-group 31 mode on
no nameif
no security-level
no ip address
Configure Master, Sync to Slaves via CCL link
Notes: Interface security levels and traffic filtering parameters are dependent on customer security policies. For the purposes of testing security level 100 is used, and traffic is allowed to traverse between interfaces of the same security level.

## Slide 72
Flow Owners can be predetermined during steady state operation
Flow Ownership can be predetermined during fail events*
Ease of connection tracking during troubleshooting efforts
ITD + ASA Clustering Benefits

## Slide 73: ITD Functionality: ASA Clustering Flow Owner Predictability without ITD
x.x.x..0 - .255
Flow ownership cannot be pre-determined easily by network engineers. Traffic from any source can go to any ASA.
Difficult to trace connections across cluster without debugging

## Slide 74
BUCKET 1 - 10 permit ip 1.1.1.0 255.255.255.63 VIP
ITD NODE 1 – Owns all flows for Bucket 1
BUCKET 2 - 10 permit ip 1.1.1.64 255.255.255.63 VIP
ITD NODE 2 – Owns all flows for Bucket 2
BUCKET 3 - 10 permit ip 1.1.1.128 255.255.255.63 VIP
ITD NODE 3 – Owns all flows for Bucket 3
BUCKET 4 - 10 permit ip 1.1.1.192 255.255.255.63 VIP
ITD NODE 4 – Owns all flows for Bucket 4
.0 - .63
.64 - .127
.128 - .191
.192 - .255
ITD Functionality: ASA Clustering Flow Owner Predictability with ITD
Instead of flow ownership being determined by ECMP or port-channel hashing algorithm, ITD bucket allocation determines flow owner

## Slide 75
ITD
Auto Configuration

## Slide 76
Nexus 7000
Automatic Configuration
Once the ITD Process is enabled (per ‘no shut’ CLI), the following elements are automatically added to the configuration:
ACLs that define bucket assignments are configured
Route-Maps are configured that associate the ACL bucket assignments to individual firewalls as next-hops (ITD nodes)
Route-Maps are applied to ingress interfaces of the traffic flow
If ITD Probes are configured, IP SLA is configured in the background to send probes to each ITD defined in the ITD device group
The following automatic configuration in the slides that follow was applied using the ‘firewall on a stick’ deployment configuration with the option of allocating 16 buckets (across 4 firewalls).

## Slide 77
#INSIDE
ip access-list INSIDE_itd_bucket_1
10 permit ip 1.1.1.0 255.255.255.15 any
ip access-list INSIDE_itd_bucket_2
10 permit ip 1.1.1.16 255.255.255.15 any
ip access-list INSIDE_itd_bucket_11
10 permit ip 1.1.1.160 255.255.255.15 any
ip access-list INSIDE_itd_bucket_12
10 permit ip 1.1.1.176 255.255.255.15 any
ip access-list INSIDE_itd_bucket_13
10 permit ip 1.1.1.192 255.255.255.15 any
ip access-list INSIDE_itd_bucket_14
10 permit ip 1.1.1.208 255.255.255.15 any
ip access-list INSIDE_itd_bucket_15
10 permit ip 1.1.1.224 255.255.255.15 any
ip access-list INSIDE_itd_bucket_16
10 permit ip 1.1.1.240 255.255.255.15 any
ip access-list INSIDE_itd_bucket_3
10 permit ip 1.1.1.32 255.255.255.15 any
ip access-list INSIDE_itd_bucket_4
10 permit ip 1.1.1.48 255.255.255.15 any
ip access-list INSIDE_itd_bucket_5
10 permit ip 1.1.1.64 255.255.255.15 any
ip access-list INSIDE_itd_bucket_6
10 permit ip 1.1.1.80 255.255.255.15 any
ip access-list INSIDE_itd_bucket_7
10 permit ip 1.1.1.96 255.255.255.15 any
ip access-list INSIDE_itd_bucket_8
10 permit ip 1.1.1.112 255.255.255.15 any
ip access-list INSIDE_itd_bucket_9
10 permit ip 1.1.1.128 255.255.255.15 any
ip access-list INSIDE_itd_bucket_10
10 permit ip 1.1.1.144 255.255.255.15 any
#OUTSIDE
p access-list OUTSIDE_itd_bucket_1
10 permit ip any 1.1.1.0 255.255.255.15
ip access-list OUTSIDE_itd_bucket_2
10 permit ip any 1.1.1.16 255.255.255.15
ip access-list OUTSIDE_itd_bucket_11
10 permit ip any 1.1.1.160 255.255.255.15
ip access-list OUTSIDE_itd_bucket_12
10 permit ip any 1.1.1.176 255.255.255.15
ip access-list OUTSIDE_itd_bucket_13
10 permit ip any 1.1.1.192 255.255.255.15
ip access-list OUTSIDE_itd_bucket_14
10 permit ip any 1.1.1.208 255.255.255.15
ip access-list OUTSIDE_itd_bucket_15
10 permit ip any 1.1.1.224 255.255.255.15
ip access-list OUTSIDE_itd_bucket_16
10 permit ip any 1.1.1.240 255.255.255.15
ip access-list OUTSIDE_itd_bucket_3
10 permit ip any 1.1.1.32 255.255.255.15
ip access-list OUTSIDE_itd_bucket_4
10 permit ip any 1.1.1.48 255.255.255.15
ip access-list OUTSIDE_itd_bucket_5
10 permit ip any 1.1.1.64 255.255.255.15
ip access-list OUTSIDE_itd_bucket_6
10 permit ip any 1.1.1.80 255.255.255.15
ip access-list OUTSIDE_itd_bucket_7
10 permit ip any 1.1.1.96 255.255.255.15
ip access-list OUTSIDE_itd_bucket_8
10 permit ip any 1.1.1.112 255.255.255.15
ip access-list OUTSIDE_itd_bucket_9
10 permit ip any 1.1.1.128 255.255.255.15
ip access-list OUTSIDE_itd_bucket_10
10 permit ip any 1.1.1.144 255.255.255.15
ACLs that define bucket assignments are configured
Auto Configuration – Nexus 7000

## Slide 78
#INSIDE
route-map INSIDE_itd_pool permit 0
match ip address INSIDE_itd_bucket_1
set ip next-hop verify-availability 10.1.0.111 track 11
route-map INSIDE_itd_pool permit 1
match ip address INSIDE_itd_bucket_2
set ip next-hop verify-availability 10.1.0.112 track 13
route-map INSIDE_itd_pool permit 2
match ip address INSIDE_itd_bucket_3
set ip next-hop verify-availability 10.1.0.113 track 15
route-map INSIDE_itd_pool permit 3
match ip address INSIDE_itd_bucket_4
set ip next-hop verify-availability 10.1.0.114 track 17
route-map INSIDE_itd_pool permit 4
match ip address INSIDE_itd_bucket_5
set ip next-hop verify-availability 10.1.0.111 track 11
route-map INSIDE_itd_pool permit 5
match ip address INSIDE_itd_bucket_6
set ip next-hop verify-availability 10.1.0.112 track 13
route-map INSIDE_itd_pool permit 6
match ip address INSIDE_itd_bucket_7
set ip next-hop verify-availability 10.1.0.113 track 15
route-map INSIDE_itd_pool permit 7
match ip address INSIDE_itd_bucket_8
set ip next-hop verify-availability 10.1.0.114 track 17
route-map INSIDE_itd_pool permit 8
match ip address INSIDE_itd_bucket_9
set ip next-hop verify-availability 10.1.0.111 track 11
route-map INSIDE_itd_pool permit 9
match ip address INSIDE_itd_bucket_10
set ip next-hop verify-availability 10.1.0.112 track 13
Route-Maps are configured that associate the ACL bucket assignments to individual firewalls as next-hops (ITD nodes)
Auto Configuration – Nexus 7000
route-map INSIDE_itd_pool permit 10
match ip address INSIDE_itd_bucket_11
set ip next-hop verify-availability 10.1.0.113 track 15
route-map INSIDE_itd_pool permit 11
match ip address INSIDE_itd_bucket_12
set ip next-hop verify-availability 10.1.0.114 track 17
route-map INSIDE_itd_pool permit 12
match ip address INSIDE_itd_bucket_13
set ip next-hop verify-availability 10.1.0.111 track 11
route-map INSIDE_itd_pool permit 13
match ip address INSIDE_itd_bucket_14
set ip next-hop verify-availability 10.1.0.112 track 13
route-map INSIDE_itd_pool permit 14
match ip address INSIDE_itd_bucket_15
set ip next-hop verify-availability 10.1.0.113 track 15
route-map INSIDE_itd_pool permit 15
match ip address INSIDE_itd_bucket_16
set ip next-hop verify-availability 10.1.0.114 track 17

## Slide 79
#OUTSIDE
route-map OUTSIDE_itd_pool permit 0
match ip address OUTSIDE_itd_bucket_1
set ip next-hop verify-availability 10.0.0.111 track 20
route-map OUTSIDE_itd_pool permit 1
match ip address OUTSIDE_itd_bucket_2
set ip next-hop verify-availability 10.0.0.112 track 22
route-map OUTSIDE_itd_pool permit 2
match ip address OUTSIDE_itd_bucket_3
set ip next-hop verify-availability 10.0.0.113 track 24
route-map OUTSIDE_itd_pool permit 3
match ip address OUTSIDE_itd_bucket_4
set ip next-hop verify-availability 10.0.0.114 track 26
route-map OUTSIDE_itd_pool permit 4
match ip address OUTSIDE_itd_bucket_5
set ip next-hop verify-availability 10.0.0.111 track 20
route-map OUTSIDE_itd_pool permit 5
match ip address OUTSIDE_itd_bucket_6
set ip next-hop verify-availability 10.0.0.112 track 22
route-map OUTSIDE_itd_pool permit 6
match ip address OUTSIDE_itd_bucket_7
set ip next-hop verify-availability 10.0.0.113 track 24
route-map OUTSIDE_itd_pool permit 7
match ip address OUTSIDE_itd_bucket_8
set ip next-hop verify-availability 10.0.0.114 track 26
route-map OUTSIDE_itd_pool permit 8
match ip address OUTSIDE_itd_bucket_9
set ip next-hop verify-availability 10.0.0.111 track 20
route-map OUTSIDE_itd_pool permit 9
match ip address OUTSIDE_itd_bucket_10
set ip next-hop verify-availability 10.0.0.112 track 22
Route-Maps are configured that associate the ACL bucket assignments to individual firewalls as next-hops (ITD nodes)
Auto Configuration – Nexus 7000
route-map OUTSIDE_itd_pool permit 10
match ip address OUTSIDE_itd_bucket_11
set ip next-hop verify-availability 10.0.0.113 track 24
route-map OUTSIDE_itd_pool permit 11
match ip address OUTSIDE_itd_bucket_12
set ip next-hop verify-availability 10.0.0.114 track 26
route-map OUTSIDE_itd_pool permit 12
match ip address OUTSIDE_itd_bucket_13
set ip next-hop verify-availability 10.0.0.111 track 20
route-map OUTSIDE_itd_pool permit 13
match ip address OUTSIDE_itd_bucket_14
set ip next-hop verify-availability 10.0.0.112 track 22
route-map OUTSIDE_itd_pool permit 14
match ip address OUTSIDE_itd_bucket_15
set ip next-hop verify-availability 10.0.0.113 track 24
route-map OUTSIDE_itd_pool permit 15
match ip address OUTSIDE_itd_bucket_16
set ip next-hop verify-availability 10.0.0.114 track 26

## Slide 80
#INSIDE
interface Vlan1101
ip policy route-map INSIDE_itd_pool
#OUTSIDE
interface Vlan1001
ip policy route-map OUTSIDE_itd_pool
Route-Maps are applied to ingress interfaces of the traffic flow
Auto Configuration – Nexus 7000

## Slide 81
#INSIDE
ip sla 10001
icmp-echo 10.1.0.111
frequency 5
ip sla schedule 10001 life forever start-time now
ip sla 10002
icmp-echo 10.1.0.112
frequency 5
ip sla schedule 10002 life forever start-time now
ip sla 10003
icmp-echo 10.1.0.113
frequency 5
ip sla schedule 10003 life forever start-time now
ip sla 10004
icmp-echo 10.1.0.114
frequency 5
ip sla schedule 10004 life forever start-time now
#OUTSIDE
ip sla 10006
icmp-echo 10.0.0.111
frequency 5
ip sla schedule 10001 life forever start-time now
ip sla 10007
icmp-echo 10.0.0.112
frequency 5
ip sla schedule 10002 life forever start-time now
ip sla 10008
icmp-echo 10.0.0.113
frequency 5
ip sla schedule 10003 life forever start-time now
ip sla 10009
icmp-echo 10.0.0.114
frequency 5
ip sla schedule 10004 life forever start-time now
If ITD Probes are configured, IP SLA is configured in the background to send probes to each ITD defined in the ITD device group
Auto Configuration – Nexus 7000
track 1 ip sla 10001 reachability
delay down 1
track 2 ip sla 10002 reachability
delay down 1
track 3 ip sla 10003 reachability
delay down 1
track 4 ip sla 10004 reachability
delay down 1
track 5 interface Vlan1101 line-protocol
Track 6 ip sla 10006 reachability
delay down 5
Track 7 ip sla 10007 reachability
delay down 5
Track 8 ip sla 10008 reachability
delay down 5
Track 9 ip sla 10009 reachability
delay down 5
track 10 interface Vlan1001 line-protocol

## Slide 82
#INSIDE
route-map INSIDE_itd_pool pbr-statistics
#OUTSIDE
route-map OUTSIDE_itd_pool pbr-statistics
To enable statistics gathering, enable ‘route-map <route-map-name> pbr-statistics’ after enabling the ITD process
Configuration Steps – Nexus 7000

## Slide 83
DC1-N7K-7(config)# show itd brief
Name Probe LB Scheme Interface Status Buckets
-------------- ----- ---------- ---------- -------- --------
INSIDE ICMP src-ip Vlan1101 ACTIVE 16
Device Group
--------------------------------------------------
FW_INSIDE
Virtual IP Netmask/Prefix Protocol Port
------------------------------------------------------ ------------ ----------
10.1.0.110 / 255.255.255.255 IP 0
Node IP Config-State Status Track_id Sla_id
--------------------------------- ------------ ---------- --------- ---------
1 10.1.0.111 Active OK 1 10001
2 10.1.0.112 Active OK 2 10002
3 10.1.0.113 Active OK 3 10003
4 10.1.0.114 Active OK 4 10004
‘show itd brief’ displays high level ITD parameters applied to each firewall node.
This output uses the ‘firewall on a stick’ topology with 2 ITD processes in the same VDC.
ITD Verification – Nexus 7000
Name Probe LB Scheme Interface Status Buckets
-------------- ----- ---------- ---------- -------- --------
OUTSIDE ICMP dst-ip Vlan1100 ACTIVE 16
Device Group
--------------------------------------------------
FW_OUTSIDE
Virtual IP Netmask/Prefix Protocol Port
------------------------------------------------------ ------------ ----------
10.0.0.110 / 255.255.255.255 IP 0
Node IP Config-State Status Track_id Sla_id
--------------------------------- ------------ ---------- --------- ---------
1 10.0.0.111 Active OK 6 10006
2 10.0.0.112 Active OK 7 10007
3 10.0.0.113 Active OK 8 10008
4 10.0.0.114 Active OK 9 10009

## Slide 84
DC1-N7K-7# show itd
Name Probe LB Scheme Status Buckets
-------------- ----- ---------- -------- -------
INSIDE ICMP src-ip ACTIVE 16
Device Group
--------------------------------------------------
FW_INSIDE
Route Map Interface Status Track_id
------------------------------ ------------ ------ ---------
INSIDE_itd_pool Vlan1101 UP 5
Virtual IP Netmask/Prefix Protocol Port
------------------------------------------------------ ------------ ----------
10.1.0.110 / 255.255.255.255 IP 0
Node IP Config-State Status Track_id Sla_id
--------------------------------- ------------ ---------- --------- ---------
1 10.1.0.111 Active OK 1 10001
IP Access List
-----------------------------------------------------------------------
INSIDE_itd_vip_1_bucket_1
INSIDE_itd_vip_1_bucket_5
INSIDE_itd_vip_1_bucket_9
INSIDE_itd_vip_1_bucket_13
‘show itd’ displays ITD parameters applied to each firewall including bucket distribution.
ITD Verification – Nexus 7000
Node IP Config-State Status Track_id Sla_id
--------------------------------- ------------ ---------- --------- ---------
2 10.1.0.112 Active OK 2 10002
IP Access List
-----------------------------------------------------------------------
INSIDE_itd_vip_1_bucket_2
INSIDE_itd_vip_1_bucket_6
INSIDE_itd_vip_1_bucket_10
INSIDE_itd_vip_1_bucket_14
Node IP Config-State Status Track_id Sla_id
--------------------------------- ------------ ---------- --------- ---------
3 10.1.0.113 Active OK 3 10003
IP Access List
-----------------------------------------------------------------------
INSIDE_itd_vip_1_bucket_3
INSIDE_itd_vip_1_bucket_7
INSIDE_itd_vip_1_bucket_11
INSIDE_itd_vip_1_bucket_15
Node IP Config-State Status Track_id Sla_id
--------------------------------- ------------ ---------- --------- ---------
4 10.1.0.114 Active OK 4 10004
IP Access List
-----------------------------------------------------------------------
INSIDE_itd_vip_1_bucket_4
INSIDE_itd_vip_1_bucket_8
INSIDE_itd_vip_1_bucket_12
INSIDE_itd_vip_1_bucket_16

## Slide 85
Name Probe LB Scheme Status Buckets
-------------- ----- ---------- -------- -------
OUTSIDE ICMP dst-ip ACTIVE 16
Device Group
--------------------------------------------------
FW_OUTSIDE
Route Map Interface Status Track_id
------------------------------ ------------ ------ ---------
OUTSIDE_itd_pool Vlan1100 UP 10
Virtual IP Netmask/Prefix Protocol Port
------------------------------------------------------ ------------ ----------
10.0.0.110 / 255.255.255.255 IP 0
Node IP Config-State Status Track_id Sla_id
--------------------------------- ------------ ---------- --------- ---------
1 10.0.0.111 Active OK 6 10006
IP Access List
-----------------------------------------------------------------------
OUTSIDE_itd_vip_1_bucket_1
OUTSIDE_itd_vip_1_bucket_5
OUTSIDE_itd_vip_1_bucket_9
OUTSIDE_itd_vip_1_bucket_13
‘show itd’ cont.
ITD Verification – Nexus 7000
Node IP Config-State Status Track_id Sla_id
--------------------------------- ------------ ---------- --------- ---------
2 10.0.0.112 Active OK 7 10007
IP Access List
-----------------------------------------------------------------------
OUTSIDE_itd_vip_1_bucket_2
OUTSIDE_itd_vip_1_bucket_6
OUTSIDE_itd_vip_1_bucket_10
OUTSIDE_itd_vip_1_bucket_14
Node IP Config-State Status Track_id Sla_id
--------------------------------- ------------ ---------- --------- ---------
3 10.0.0.113 Active OK 8 10008
IP Access List
-----------------------------------------------------------------------
OUTSIDE_itd_vip_1_bucket_3
OUTSIDE_itd_vip_1_bucket_7
OUTSIDE_itd_vip_1_bucket_11
OUTSIDE_itd_vip_1_bucket_15
Node IP Config-State Status Track_id Sla_id
--------------------------------- ------------ ---------- --------- ---------
4 10.0.0.114 Active OK 9 10009
IP Access List
-----------------------------------------------------------------------
OUTSIDE_itd_vip_1_bucket_4
OUTSIDE_itd_vip_1_bucket_8
OUTSIDE_itd_vip_1_bucket_12
OUTSIDE_itd_vip_1_bucket_16

## Slide 86
#VDC1
DC1-N7K-7(config)# show itd statistics
Service Name
--------------------------------------------------------------------
INSIDE_TRAFFIC
Virtual IP Packets
------------------------------------------------------- ------------
10.1.0.110 / 10.1.0.110 10579122
Device Group
--------------------------------------------------------------------
FW_INSIDE
Node IP Packets
----------------------------------------------------- ------------
1 10.1.0.111 2674591
IP Access List Packets
----------------------------------------------- ------------
INSIDE_TRAFFIC_itd_vip_1_bucket_1 632047
INSIDE_TRAFFIC_itd_vip_1_bucket_5 677872
INSIDE_TRAFFIC_itd_vip_1_bucket_9 654204
INSIDE_TRAFFIC_itd_vip_1_bucket_13 664108
Node IP Packets
----------------------------------------------------- ------------
2 10.1.0.112 2609811
IP Access List Packets
----------------------------------------------- ------------
INSIDE_TRAFFIC_itd_vip_1_bucket_2 629807
INSIDE_TRAFFIC_itd_vip_1_bucket_6 646168
INSIDE_TRAFFIC_itd_vip_1_bucket_10 687760
INSIDE_TRAFFIC_itd_vip_1_bucket_14 654475
‘show itd statistics’ – traffic is distributed equally across 4 firewalls using 16 buckets
ITD Verification – Nexus 7000
Node IP Packets
----------------------------------------------------- ------------
3 10.1.0.113 2674216
IP Access List Packets
----------------------------------------------- ------------
INSIDE_TRAFFIC_itd_vip_1_bucket_3 671852
INSIDE_TRAFFIC_itd_vip_1_bucket_7 669127
INSIDE_TRAFFIC_itd_vip_1_bucket_11 654682
INSIDE_TRAFFIC_itd_vip_1_bucket_15 638163
Node IP Packets
----------------------------------------------------- ------------
4 10.1.0.114 2679726
IP Access List Packets
----------------------------------------------- ------------
INSIDE_TRAFFIC_itd_vip_1_bucket_4 667743
INSIDE_TRAFFIC_itd_vip_1_bucket_8 637384
INSIDE_TRAFFIC_itd_vip_1_bucket_12 646332
INSIDE_TRAFFIC_itd_vip_1_bucket_16 645413